## Slide 1
UNIT 2 · TECHNOLOGY FOR IoT
Different Frameworks for IoT
Firmware & device-side frameworks: Arduino, ESP-IDF, FreeRTOS, and MicroPython
Arduino Framework
ESP-IDF
FreeRTOS Tasks
MicroPython
01

## Slide 2
ROADMAP
What We'll Cover Today
01
What is a "framework"?
02
Recap: the Arduino framework
03
ESP-IDF — the native framework
04
RTOS concept & FreeRTOS tasks
05
MicroPython / CircuitPython
06
Comparison & choosing the right one
02

## Slide 3
FOUNDATIONS
What Is a "Framework," Exactly?
A framework is the software layer between your code and the raw hardware.
It gives you ready-made functions (pinMode, digitalWrite...) instead of making you configure registers by hand.
You've been using one this whole time — the Arduino framework.
Different frameworks make different trade-offs:
ease of use vs control vs performance vs how many things can run "at once."
Your Sketch / App Code
Framework (Arduino / ESP-IDF / MicroPython...)
RTOS / OS Layer (often FreeRTOS)
Hardware (ESP32 chip)
↓ closer to the metal
03

## Slide 4
PART 1
Recap: The Arduino Framework
A C/C++ abstraction layer + IDE + massive library ecosystem.
On the ESP32, the Arduino framework is actually built on top of ESP-IDF underneath.
Structured around two functions: setup() (runs once) and loop() (runs forever).
This is exactly what you've used in every practical so far.
ARDUINO FRAMEWORK
void setup() {
pinMode(ledPin, OUTPUT);
}
void loop() {
digitalWrite(ledPin, HIGH);
delay(1000);
digitalWrite(ledPin, LOW);
delay(1000);
}
✓ Strengths: huge community, tons of libraries, beginner-friendly, fastest way to get something working.
04

## Slide 5
PART 1 (CONTD.)
...But Arduino Has a Catch
loop() runs everything sequentially, one line after another — nothing else happens while a line is executing.
delay() blocks the entire program. While it waits, the board can't read a sensor, respond to a button, or do anything else.
Fine for a simple blink demo. A real problem once a project needs multiple things happening "at the same time."
THE PROBLEM
delay(5000) freezes EVERYTHING for 5 full seconds — sensors, buttons, WiFi handling — all paused.
THE FIX WE'LL SEE TODAY
Two ways out: write closer to the hardware with ESP-IDF, or restructure code into independent FreeRTOS tasks that don't block each other.
05

## Slide 6
PART 2
ESP-IDF — The Native Framework
IDF = IoT Development Framework — Espressif's own official framework for the ESP32.
Written in plain C, and the Arduino-ESP32 core is actually built on top of it.
Gives direct access to low-level features Arduino hides: fine-grained WiFi config, deep-sleep tuning, precise timer/interrupt control.
Built on FreeRTOS underneath — multitasking is available natively.
ARDUINO IS BUILT ON ESP-IDF
Arduino Framework
ESP-IDF
FreeRTOS + Hardware
Trade-off: steeper learning curve, more boilerplate code — you write more to do the same simple task, in exchange for more control.
06

## Slide 7
PART 2 (CONTD.)
Same Task, Two Frameworks
Blinking an LED — Arduino framework vs raw ESP-IDF
ARDUINO
void setup() {
pinMode(2, OUTPUT);
}
void loop() {
digitalWrite(2, HIGH);
delay(1000);
digitalWrite(2, LOW);
delay(1000);
}
ESP-IDF
void app_main(void) {
gpio_set_direction(2, GPIO_MODE_OUTPUT);
while (1) {
gpio_set_level(2, 1);
vTaskDelay(1000 / portTICK_PERIOD_MS);
gpio_set_level(2, 0);
vTaskDelay(1000 / portTICK_PERIOD_MS);
}
}
07

## Slide 8
PART 2 (CONTD.)
Mapping the Concepts Across
setup() + loop()
→
app_main() with a while(1) loop inside
pinMode()
→
gpio_set_direction()
digitalWrite()
→
gpio_set_level()
delay(ms)
→
vTaskDelay(ms / portTICK_PERIOD_MS)
Same underlying idea, different level of abstraction — everything Arduino does, ESP-IDF does more explicitly.
08

## Slide 9
PART 3
Why Do We Need an RTOS?
Real IoT projects often need several things happening independently: blink an LED, read a sensor, check WiFi, respond to a button — all "at once."
A single loop() with delay() calls can't do this — one blocking call freezes everything else.
An RTOS (Real-Time Operating System) lets you split code into independent tasks that the chip switches between rapidly.
The ESP32 has FreeRTOS built in — even Arduino sketches secretly run inside one FreeRTOS task already.
ONE loop() — SEQUENTIAL
Blink LED → wait → read sensor → wait → check WiFi → ...
MULTIPLE TASKS — CONCURRENT
Task 1: Blink LED
Task 2: Read sensor
Task 3: Handle WiFi
09

## Slide 10
PART 3 (CONTD.)
FreeRTOS Tasks — In Code
xTaskCreate()
spins up a new independent task — its own function, running alongside everything else.
Inside a task, vTaskDelay()
pauses only that task — other tasks keep running.
You can create a task from setup() itself, even in the Arduino framework, using its underlying FreeRTOS support.
loop() can end up doing nothing at all — the real work happens in tasks.
ARDUINO + FreeRTOS
void blinkTask(void *pvParameters) {
pinMode(2, OUTPUT);
while (1) {
digitalWrite(2, HIGH);
vTaskDelay(500 / portTICK_PERIOD_MS);
digitalWrite(2, LOW);
vTaskDelay(500 / portTICK_PERIOD_MS);
}
}
void setup() {
xTaskCreate(blinkTask, "Blink", 1000, NULL, 1, NULL);
}
void loop() {
// empty -- task handles blinking
}
10

## Slide 11
PART 3 (CONTD.)
FreeRTOS Tasks — In Code
xTaskCreate()
xTaskCreate(blinkTask, "Blink", 1000, NULL, 1, NULL);
10
# | Argument | Example Value | Meaning
1 | Function | blinkTask | Which function becomes the new task
2 | Name | "Blink" | Just a label, useful for debugging (shows up in task lists)
3 | Stack size | 1000 | How many bytes of stack this task gets — separate from the main loop() task's stack
4 | Parameters | NULL | Nothing passed into blinkTask's pvParameters (used to pass data into the task at creation)
5 | Priority | 1 | Scheduling priority — higher number = runs more eagerly when tasks compete for CPU time
6 | Task handle | NULL | Not keeping a reference to control/delete this task later

## Slide 12
PART 3 (CONTD.)
delay() vs vTaskDelay() — The Key Difference
delay()
Freezes the ENTIRE program.
Nothing else can run — no other task, no sensor check, nothing.
Fine only when nothing else needs to happen during the wait.
vTaskDelay()
Pauses only the CURRENT task.
Other tasks keep running normally during that time.
This is what makes true multitasking possible on the ESP32.
11

## Slide 13
PART 4
MicroPython / CircuitPython
A completely different approach: write and run actual Python directly on the microcontroller.
No separate compile step — flash MicroPython once, then just copy/edit .py files onto the board.
Comes with a REPL — an interactive prompt where you can type a command and see it run instantly on the hardware.
CircuitPython (by Adafruit) is a friendly variant, popular in education and beginner boards.
WHY IT FEELS DIFFERENT
No compiling — edit → save → it just runs
Interactive REPL — type a line, see it execute live
Python syntax — no semicolons, no curly braces
12

## Slide 14
PART 4 (CONTD.)
Same Blink, in MicroPython
ARDUINO (C++)
void setup() {
pinMode(2, OUTPUT);
}
void loop() {
digitalWrite(2, HIGH);
delay(1000);
digitalWrite(2, LOW);
delay(1000);
}
MICROPYTHON
from machine import Pin
import time
led = Pin(2, Pin.OUT)
while True:
led.value(1)
time.sleep(1)
led.value(0)
time.sleep(1)
13

## Slide 15
PART 4 (CONTD.)
MicroPython — Trade-offs
✓ ADVANTAGES
Much faster to prototype — no compile/upload cycle.
Interactive REPL for quick testing and debugging.
Gentler syntax — great for teaching programming concepts.
✗ LIMITATIONS
Slower execution than compiled C/C++.
Higher RAM overhead — less headroom for large projects.
Not ideal for tight timing or high-performance tasks.
14

## Slide 16
PART 5
Framework Comparison
FRAMEWORK
BEST FOR
LEARNING CURVE
MULTITASKING
Arduino
Quick prototypes, learning, huge library support
Low
Manual only
ESP-IDF
Production firmware, fine-grained hardware control
High
Native (FreeRTOS)
FreeRTOS tasks
Multiple concurrent operations in real products
Medium–High
Native
MicroPython
Rapid scripting, education, quick experiments
Low
Limited
15

## Slide 17
PART 5 (CONTD.)
Which One Should I Actually Use?
Just starting out / a class project?
Arduino framework
Need max performance or deep hardware access?
ESP-IDF
Project needs several things running independently?
FreeRTOS tasks
Want to prototype fast, or learning programming basics?
MicroPython
16

## Slide 18
RECAP
What You Should Take Away
Framework
= the abstraction layer between code and hardware — you've always used one.
Arduino
= easiest to start, but single-threaded and delay() blocks everything.
ESP-IDF
= native, more control, more code — what Arduino is built on.
FreeRTOS tasks
= the real fix for "multiple things at once" — vTaskDelay() doesn't block other tasks.
MicroPython
= fastest to prototype, but slower and less memory-efficient than compiled C.
17