## Slide 1: Zigbee

## Slide 2: Intro to Zigbee
Wireless communication protocol based on IEEE 802.15.4
Short-range, low-data-rate, low-power use
Designed mainly for Internet of Things (IoT)
Optimized for energy efficiency, reliability, scalability
Used in smart homes, industry, healthcare, and energy systems

## Slide 3: Key Features
10–100 m indoors (extendable with mesh routing)
Up to 250 kbps (sufficient for control & sensors)
Supports Star, Tree, Mesh topologies
Coordinator, Router, End Device
2.4 GHz (global), 868 MHz (EU), 915 MHz (US)
Low-cost, highly scalable, secure communication
Range
Data Rate
Frequencies
Topologies
Device Types
Benefits

## Slide 4: Why Named Zigbee?
Inspired by honeybees’ waggle dance – zigzag communication
Represents efficiency, teamwork,
and coordination
Zig = zigzag dance
Bee = cooperative community
Devices form a resilient
self-healing mesh network like
bees
Zig
Combined
Bee
Overall

## Slide 5: Timeline
IEEE starts 802.15.4 standard
Zigbee Alliance founded
First Zigbee specification
Zigbee IP with IPv6 support
Zigbee PRO with stronger security & scalability
Zigbee 2006 with improved interoperability
1998
2002
2004
2013
2007
2006
Zigbee 3.0 unified versions
2016-2017
Major role in IoT ecosystems
Present Day

## Slide 6: Layers in Zigbee
modulation, transmission, reception
manages wireless channel access
routing, addressing, security
end-user IoT applications
Physical Layer (PHY)
Application Support Layer (APS)
Application Framework
MAC Layer
Network Layer (NWK)
bridges network & apps

## Slide 7: Topologies
hierarchical parent-child
connections (scalable)
central coordinator as hub (simple but single point of failure)
devices relay data, robust and self-healing
Tree
Star
Mesh

## Slide 8: Part 1: Setup & Roles
creates & manages the network
forwards data, extends coverage
battery-powered, communicates via parent, supports sleep mode
Coordinator sets channel, ID, security
Network Formation
Coordinator
Router
End Device

## Slide 9: Part 2: Communication
devices send small data packets
enable multi-hop mesh routing
128-bit AES encryption ensures safe data transfer
If path fails, alternate routes used
Routers
Self Healing
Security
Communication
end devices mostly sleep, wake to send/receive
Low Power Operation

## Slide 10: Advantages
Ultra-low power consumption → years of battery life
Reliable – self-healing mesh ensures communication
Secure – AES-128 encryption
Highly scalable – supports thousands of devices
Low cost – cheaper than Wi-Fi/Bluetooth

## Slide 11: Limitations
Latency in Mesh Networks
Multi-hop communication introduces delays. Not ideal for real-time or time-critical applications.
Interference
Operates mostly on the 2.4 GHz ISM band, where Wi-Fi, Bluetooth, and even microwave ovens also operate. Can suffer from congestion and signal overlap in crowded environments.
Range
Typically supports 10–100 meters indoors depending on walls and interference. Extended range requires mesh networking, but without enough intermediate devices, coverage is limited.
Low data rate
Maximum speed is 250 kbps, which is much lower than Wi-Fi or Bluetooth. Not suitable for bandwidth-heavy applications like video or large file transfer.

## Slide 12: Applications
irrigation, soil monitoring
smart meters, grid integration
patient tracking, medical devices
monitoring, predictive maintenance
Agriculture
Healthcare
Industrial IoT
Energy
lighting, thermostats, security
Smart Home

## Slide 13: Thank You